## Slide 1
Detailed Routing
Shoukath Ali Mohammad
6819945
Topics in Systems Engineering - IC Design

## Slide 2: Index
Introduction to Detailed Routing
Constraints in Detailed Routing
Channel Routing
Switch Box Routing
Over the Cell Routing(OTC)
Summary
References

## Slide 3: Introduction to Detailed Routing
  Next to Global routing
  Consider the routing regions one at a time
  Detailed routing is finding the actual geometric layout paths
  Layout of two different nets should not intersect on the same layer
Detailed Routing
Global Routing

## Slide 4: Introduction to Detailed Routing
A
B
B
C
0
C
C
A
A
0
net
branch
trunk
tracks
terminal
Terminology:

## Slide 5: Constraints in Detailed Routing
Horizontal Constraints
Vertical Constraints
Problem : The horizontal span of two terminals occupy common area
Solution : Each terminal should be assigned to separate tracks.
A
B
B
A
0
0
0
0
span
terminal
net
Horizontal Constraints

## Slide 6: Constraints in Detailed Routing
: number of tracks.
A
E
B
0
B
A
A
0
C
D
0
C
0
A
B
E
D
0
0
B
C
C
A
B
C
D
E
A
B
C
D
E
a b c d e f g h i j k :Column
S(a) = {A,C}, S(b) = {A,C,E}, S(c) = {A,B,C,E}, S(d) = {A,B,C,E},
S(e) = {A,B,C,E}
S(f) = {A,B,C}, S(g) = {A,B,C,D}, S(h) = {B,C,D}, S(i) = {B,C,D},
S(j) = {B,C,D}, S(k) = {C}
net/vertex
constraint/edge
Fig: HCG(undirected)
Horizontal constraint graph
S =
Reference: Detailed routing by Andrew B. Kahng

## Slide 7: Constraints in Detailed Routing
Problem : When two terminals have pins in the same column.
Solution : Terminal on the top must be assigned a track above that of the lower terminal.
Vertical Constraints
A
E
B
0
B
A
A
0
C
D
0
C
0
A
B
E
D
0
0
B
C
C
Fig: VCG(directed)
terminal
Vertical constraint graph
: assignment of order of nets to tracks.
A
B
C
D
E
net
edge
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng

## Slide 8: Constraints in Detailed Routing
Problem : When two terminals have pins in the same column.
Solution : Terminal on the top must be assigned a track above that of the lower terminal.
Vertical Constraints
Fig: VCG(directed)
A
B
B
B
0
A
A
B
A
B
B
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng

## Slide 9: Channel Routing
Channel Routing is a special case of detailed routing where pins are on either side of a channel and are routed on a horizontal routing region
Channel Routing Algorithms
  Left-Edge Algorithm
  Dogleg Routing Algorithm

## Slide 10: Channel Routing
Channel Routing is a special case of detailed routing where pins are on either side of a channel and are routed on a horizontal routing region
Based on the VCG and the left-edge order
Left-edge order and VCG are used to determine the assignment order of terminals to tracks
HCG can be used to check no of tracks to be used
Only one horizontal segment is allowed to use by each terminal
Left-Edge Algorithm

## Slide 11: Channel Routing
Left-Edge Algorithm example:
0
A
D
E
A
F
G
0
D
I
J
J
B
C
E
C
E
B
F
H
G
I
I
H
Generate VCG and Left-edge order
A
J
D
E
I
G
C
H
F
B
Left edge order = {B, A, C, D, E, F, G, H, I, J}
Fig : VCG
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng

## Slide 12: Channel Routing
Left edge order = {B, A, C, D, E, F, G, H, I, J}
0
A
D
E
A
F
G
0
D
I
J
J
B
C
E
C
E
B
F
H
G
I
I
H
A
J
D
E
I
G
C
H
F
B
1
2
3
4
5
Fig : VCG

## Slide 13: Channel Routing
Improving left-edge algorithm by net splitting
Two advantages:
  Alleviate conflicts in VCG
  Number of tracks can often be reduced
Dogleg
Net splitting
Dogleg Routing Algorithm
Reference: Detailed routing by Andrew B. Kahng

## Slide 14: Channel Routing
A
A
B
0
B
0
B
0
C
C
A
B
C
A
A
B
0
B
0
B
0
C
C
A
A
B
0
B
0
B
0
C
C
A
B1
B2
C
A
B1
B2
C
(a) Channel routing problem
(b) VCG without net splitting
(c) Channel routing solution
(d) Net splitting
(e) VCG with net splitting
0
B
0
C
C
(f) Channel routing solution
A
A
B
B
0
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng
Reference: Detailed routing by Andrew B. Kahng

## Slide 15: Channel Routing
Example:
A
A
B
0
B
C
B
C
0
C
D
D
A
B1
B2
C1
C2
D
B
C
D
A
B1
C1
A
B2
C2
D
Fig : VCG(actual)
Fig : VCG(modified)

## Slide 16: Channel Routing
A
A
B
0
B
C
B
C
0
C
D
D
B1
C1
A
B2
C2
D
B1,B2
B1
B2
C2
C1
C1,C2
Left edge order = {A, B1, C1, B2, C2, D}

## Slide 17: Switch Box Routing
Pins on all four directions of a fixed-size grid based routing region
More complex than channel routing
Horizontal tracks or vertical columns can be assigned on a single layer
When routing fails new tracks are laid
Algorithm for switch box routing can be derived from channel routing algorithms
A horizontal track is automatically assigned to a pin on the left

## Slide 18: Switch Box Routing
Example:
TOP = [0 D F H E C C]
LEFT = [A 0 D F G 0]
BOT = [0 0 G H B B H]
RIGHT = [B H A C E C]
Fig: Switchbox routing problem
6 0
5 G
4 F
3 D
2 0
1 A
C
E
C
A
H
B
a b c d e f g
0 D F H E C C
0 0 G H B B H
Tracks
Columns
Reference: Detailed routing by Andrew B. Kahng
(Reference: Detailed routing by Andrew B. Kahng)

## Slide 19: Over The Cell Routing
For routing more than three layers
Higher metal layers like Metal2 and Metal3 pins are used
Standard cells are not obstructed for these layers are not by the
Routing is performed on the entire chip area
Fig: OTC routing with two metal layers
Source: Detailed routing by Andrew B. Kahng

## Slide 20: Over The Cell Routing
Chameleon OTC router
Developed by Braun et al.
Generates topologies for nets in either two or three metal layers
Minimise the total routing area
Assigns net segments to tracks
Ability to take into account technology parameters on a per layer basis
Designer can specify the wire width and the minimum distance between each wire segment for each layer
( Source: Detailed routing by Andrew B. Kahng)

## Slide 21: Summary
Detailed routing is invoked after global routing
Horizontal and Vertical constraints must be satisfied by valid routes
Channels have net terminals on the two sides
Switch-boxes have terminals on four sides
Channels are joined as switchboxes
When the number of metal layers in greater than 3, use over the cell (OTC) routing

## Slide 22: Reference
VLSI Physical Design: From Graph Partitioning to Timing Closure by Andrew B. Kahng, Jens Lienig, Igor L. Markov, Jin Hu

## Slide 23
Shoukath Ali Mohammad
6819945
Thankyou for your attention